## Slide 1: IoT for Industrial Controls
Design Exploration, SDK, and Standards
Michael J Koster
November 26, 2020

## Slide 2: Scope
Apply IoT industry learning to Industrial Controls
Abstraction of Communication Protocols using IoT patterns and technology - OneFieldBus
Model-driven design using SDF with existing standards
Map PLC programming patterns onto a distributed control fabric
SDK Approach to deliver a reference platform
Open Standards and Open Source Runtime

## Slide 3: End-to-end Model Driven Design
Use SDF and SDF extensions to model system elements – architecture neutral and developer friendly
Map to RDF and connect to existing ontologies
Process Model – P&ID data, Digital Twin Modeling
Instrumentation and Control Points
Control networks – Control Loop Diagrams
Function blocks – IEC 61499
Application logic – Inside Function Blocks

## Slide 4: SDK Outline
SDF Models
LWM2M Objects
C++ Modules Implementation
NodeJS Modules Implementation
C++ Embedded Stack – Event Loop
Node-RED Runtime Framework
System Runtime
Process GUI
IEC 61499 Function Blocks
Code Gen
Code Gen
Startup, Configuration, Management
Operator, Engineering Consoles
Real-time process & networking

## Slide 5: Modeling in SDF and Extensions
Function Block – Properties, Actions, Events
Internal Logic– Application Logic, State Machines
Common Data Types; Quantities, Units, Scales
Alarms and Reports, Logging
Fieldbus Message formats and Protocols
System Logic – Brokers, Servers, Descriptors
Process Modeling – P&ID and Digital Twin Models
Control Points and Control Networks

## Slide 6: Standardization Opportunities
Function Blocks for common applications, PID controllers, sensors and actuators, sequencer controllers, programmed logic
SDF language extensions for control systems + RDF mapping and integration with common ontologies
Mapping LWM2M Objects to PubSub protocol
Models for system elements

## Slide 7: Physical Testbed and Demo
Industrial/medical Gas Separator
Air compressor, Air Dryer, and Pressure Swing Adsorption units
Continuous and sequence controls
Safety system
Also represents an integrated product/SKU level configurations

## Slide 8: SDK
Tool flow
System tools and components
Models
Control System Architecture

## Slide 9: SDK Tool Flow
Translator
Code Gen
SDF Models
LWM2M Models
IEC 61499 Models
OPC-UA Models
SDF Mapping Files
Target
Files
System Config Manifest
Target
Files
Node-RED,
C++/Arduino
W3C WoT TD
W3C WoT TD
SDF + Mapping Files
Instrument and Control System Design
Node-wot, Digital Twin

## Slide 10: System Tools and Components
System design tools and configuration manifest
Control loop and sub-system modeling
Centralized logging and alarms
Digital Twin framework

## Slide 11: Models
(SDK Developed)
Control system models for PLC functionality
Continuous and batch process control elements
State machines, Programmers, Sequencers
HMI models
(Externally sourced)
P&ID process models => digital twin
Process ontologies and vocabularies
Control algorithm abstract models
Quantities and Units

## Slide 12: Control System Architecture
Embedded module integrations use LWM2M Object links
Pub/Sub - Serial and MQTT bearers initially
  LoRA and USB through serial pub/sub bearer
  Publisher and Subscriber Modules to customize the communication stack and adapt to Field Buses
Example Transmitter as Sensor + Publisher
Example Controller
Local and FieldBus integration patterns
System Architecture Example

## Slide 13: Integration Patterns – FieldBus
Sensor
Publisher
Subscriber
Actuator
FieldBus
Fieldbus Transmitter
FieldBus
Fieldbus Receiver

## Slide 14: Integration Patterns - Modular Controller Example
Input
Output
Controller
Setpoint
Settings
LWM2M Object Links to internal function blocks

## Slide 15: Integration Patterns – Local Controller Integration
Input
Output
Controller
Setpoint
Settings
Actuator
Sensor
HMI
LWM2M Object Links to locally integrated function blocks

## Slide 16: Integration Patterns – FieldBus Controller Integration
Input
Output
Controller
Setpoint
Settings
Publisher
Subscriber
Subscriber
FieldBus Points
Pub/Sub Integrated
Function Blocks

## Slide 17: System Architecture Example
Node-RED
MQTT Broker
Node-WoT
Embedded RTU
Embedded RTU, Loop Controller
Digital Twin
HTTP, CoAP
PLC Brain, Embedded Linux
PLC Equivalent
(Brain + RTUs)
Local
USB, WiFi, PoE
GUI
HMI
Actuators
Sensors
GPIO